## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #1
Introduction
From High-Level Languages to Computer Organisation
(AY2019/20 Semester 2)

## Slide 2: Lecture #1: Introduction
Programming Languages
C Programming Language
Abstraction
So, What is a Computer?
Why Study Computer Organisation?

## Slide 3
1. Programming Languages (1/5)
Programming language: a formal language that specifies a set of instructions for a computer to implement specific algorithms to solve problems.

## Slide 4
1. Programming Languages (2/5)
High-level program
Eg: C (CS1010), Java (CS1010J), Python (CS1010S), ECMAScript (CS1101S)
int i, a = 0;
for (i=1; i<=10; i++) {
a = a + i*i;
}
Low-level program
Eg: MIPS (CS2100)
addi $t1, $zero, 10
add $t1, $t1, $t1
addi $t2, $zero, 10
Loop: addi $t2, $t2, 10
addi $t1, $t1, -1
beq $t1, $zero, Loop
Machine code
00100000000010010000000000001010
00000001001010010100100000100000
. . .
Computers can execute only machine code directly.
a = 0
for i in range(1,11):
a = a + i*i

## Slide 5
1. Programming Languages (3/5)
1st Generation Languages
2nd Generation Languages
3rd Generation Languages
4th Generation Languages
5th Generation Languages
Machine language.
Directly executable by machine.
Machine dependent.
Efficient code but difficult to write.
Assembly language.
Need to be translated (assembled) into machine code for execution.
Efficient code, easier to write than machine code.
Closer to English.
Need to be translated (compiled or interpreted) into machine code for execution.
Eg: FORTRAN, COBOL, C, BASIC
Require fewer instructions than 3GL.
Used with databases (query languages, report generators, forms designers)
Eg: SQL, PostScript, Mathematica
Used mainly in A.I. research.
Declarative languages
Functional languages (eg: Lisp, Scheme, SML)
Logic programming (eg: Prolog)

## Slide 6
1. Programming Languages (4/5)
“Generational” classification of high level languages (3GL and later) was never fully precise.
A different classification is based on paradigm.

## Slide 7
1. Programming Languages (5/5)
Difference between scripting languages and programming languages
Scripting languages | Programming languages
Eg: JavaScript, PHP, Python | Eg: C, C++, Java
Interpreted; do not require compilation | Compiled
Generally slower | Generally faster
However, the environment is more important than the language in the classification.
  We can write a C interpreter and use it as a scripting language
  We can compile JavaScript to machine code
The distinction is getting blurred due to improved hardware capabilities and coding practices
  Eg: Python is widely used without compilation, but the main implementation (CPython) does that by compiling to bytecode on-the-fly and then running the bytecode in a VM (virtual machine)
  Eg: Java is compiled to bytecode, which is then interpreted/recompiled at runtime

## Slide 8
2. C Programming Language (1/4)
Created by Dennis Ritchie (1941 – 2011) at Bell Laboratories in the early 1970s.
C is an imperative procedural language.
C provides constructs that map efficiently to typical machine instructions.
C is a high-level language very close to the machine level, hence sometimes it is called “mid-level”.
UNIX is written in C.
#include <stdio.h>
int main(void) {
printf("Hello, world\n");
return 0;
}
HelloWorld.c
(Note: All C programs in the lectures are available on LumiNUS as well as the CS2100 website. Python versions are also available.)
print("Hello, world")
HelloWorld.py
Notes: An imperative language uses a sequence of statements to determine how to reach a certain goal. These statements are said to change the state of the program as each one is executed in turn.
A procedural language is a type of computer programming language that specifies a series of well-structured steps and procedures within its programming context to compose a program. It contains a systematic order of statements, functions and commands to complete a computational task or program.

## Slide 9
2. C Programming Language (2/4)
Creating a C program
Source code
Object code
Executable code
Editor
Linker
Compiler
Other object codes
Function libraries

## Slide 10
2. C Programming Language (3/4)
Edit
Compile and link
Execute
Illustration on SoC UNIX server

## Slide 11
2. C Programming Language (4/4)
Compile and link
The command gcc hides all the details
Using gcc –v HelloWorld.c will display all the details
The process goes through the following steps to generate machine code:
  Preprocessing
  Compilation
  Assembler
  Linker

## Slide 12
3. Abstraction (1/3)
High-level language
  Level of abstraction closer to problem domain
  Provides productivity and portability
Assembly language
  Textual and symbolic representation of instructions
Machine code (object code or binary)
  Binary bits of instructions and data

## Slide 13
3. Abstraction Layers (2/3)
Hardware/Software Stack in Computer
Application software
Operating System
Compiler
Assembler
Linker
Loader
Scheduler
Device Drivers
Processor
Memory
I/O System
Datapath & Control Design
Digital Logic Design
Circuit Design
Transistors
Software
Hardware
Instruction Set Architecture (ISA)
CS2106
CS4212
CS2100

## Slide 14
3. Abstraction (3/3)
Level of Representation

## Slide 15
4. So, What is a Computer? (1/6)
Driver
Programmer
Example: An automobile augments our power of locomotion.
A computer is a device capable of solving problems according to designed programs. It simply augments our power of storage and speed of calculation.

## Slide 16
4. So, What is a Computer? (2/6)
From computer organisation perspective, we study the components and how they work together
  Processor, memory, input/output devices, networks, …
Credit: http://tech4abc.blogspot.sg/2010/08/latest-technology-in-computer-hardwares.html

## Slide 17
4. So, What is a Computer? (3/6)
Credit: http://tech3news.com/most-recent-computer-technology/
Power supply
Motherboard
Central Processing Unit (CPU)
Random Access Memory (RAM)
Hard drive
Cooling fan
I/O devices
Credit: http://www.overclock3d.net/reviews/cpu_mainboard/the_computer_council_-_clocked_gamer_quad/1

## Slide 18
4. So, What is a Computer? (4/6)
PC motherboard
Pentium processor
Credit: http://www.computer-hardware-explained.com/what-is-a-motherboard.html
Inside a Pentium chip

## Slide 19
4. So, What is a Computer? (5/6)
Central Processing Unit
(CPU)
Control Unit
ALU
Memory Unit
Input Device
Output Device
ALU: Arithmetic/Logic Unit

## Slide 20
4. So, What is a Computer? (6/6)
Next generation…
Credit: http://www.custom-build-computers.com/Latest-Computer-Hardware.html
Credit:
http://www.prabhanjamindiaits.com/blogdetailedpage.aspx?id=66
Credit: http://new-techpc.blogspot.sg/2012/10/latest-in-computer-technology.html

## Slide 21
6th January 2014
http://www.theverge.com/2014/1/6/5282472/intel-announces-edison-a-computer-the-size-of-an-sd-card

## Slide 22
5. Why Study Computer Organisation?
Computer organisation is the study of internal working, structuring and implementation of a computer system.
It refers to the level of abstraction above the digital logic level, but below the operating system level.
CS2100

## Slide 23
5. Why Study Computer Organisation?
(From user to builder)
You want to call yourself a computer scientist/specialist.
You want to build software people use.
You need to make purchasing decisions.
You need to offer “expert” advice.
Hardware and software affect performance
  Algorithm determines number of source-level statements (eg: CS1010, CS2030, CS2040, CS3230)
  Language, compiler, and architecture determine machine instructions (COD chapters 2 and 3)
  Processor and memory determine how fast instructions are executed (COD chapters 5, 6 and 7)
Understanding performance (COD chapter 4)

## Slide 24: End of File