## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #13
Boolean Algebra

## Slide 2: Lecture #13: Boolean Algebra
Digital Circuits
Boolean Algebra
Truth Table
Precedence of Operators
Laws of Boolean Algebra
Duality
Theorems
Boolean Functions
Complement Functions
Standard Forms
Minterms and Maxterms
Canonical Forms: Sum-of-Minterms and Product-of-Maxterms

## Slide 3: 1. Digital Circuits (1/2)
Two voltage levels
  High/true/1/asserted
  Low/false/0/deasserted
Signals in digital circuit
High
Low
Signals in analog circuit
Advantages of digital circuits over analog circuits
  More reliable (simpler circuits, less noise-prone )
  Specified accuracy (determinable)
  Abstraction can be applied using simple mathematical model – Boolean Algebra
  Ease design, analysis and simplification of digital circuit – Digital Logic Design

## Slide 4: 1. Digital Circuits (2/2)
Combinational: no memory, output depends solely on the input
  Gates
  Decoders, multiplexers
  Adders, multipliers
Sequential: with memory, output depends on both input and current state
  Counters, registers
  Memories

## Slide 5: 2. Boolean Algebra
Boolean values:
  True (T or 1)
  False (F or 0)
Connectives
  Conjunction (AND)
    A  B; A  B
  Disjunction (OR)
    A + B; A  B
  Negation (NOT)
    ; ; A'
Truth tables
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | A'
0 | 1
1 | 0
Logic gates
A
B
AB
A
B
A+B
A
A'
In CS2100, we use the symbols ∙ for AND, + for OR, and ' for negation (you may use the accent bar). Please follow.

## Slide 6: 2. Boolean Algebra: AND
Do write the AND operator ∙ (instead of omitting it)
  Example: Write a∙b instead of ab
  Why? Writing ab could mean that it is a 2-bit value.

## Slide 7: 3. Truth Table
Provide a listing of every possible combination of inputs and its corresponding outputs.
  Inputs are usually listed in binary sequence.
Example
  Truth table with 3 inputs x, y, z and 2 outputs (y + z) and (x  (y + z))
x | y | z | y + z | x  (y + z)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 8: 3. Proof using Truth Table
Prove: x  (y + z) = (x  y) + (x  z)
  Construct truth table for LHS and RHS
  Check that column for LHS = column for RHS
x | y | z | y + z | x  (y + z) | x  y | x  z | (x  y) + (x  z)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

DLD page 59 Quick Review Questions Question 3-1.

## Slide 9: 4. Precedence of Operators
Precedence from highest to lowest
  Not (')
  And ()
  Or (+)
Examples:
  A  B + C = (A  B) + C
  X + Y' = X + (Y')
  P + Q'  R = P + ((Q')  R)
Use parenthesis to overwrite precedence. Examples:
  A  (B + C) [ Without parenthesis: A  B + C ]
  (P + Q)'  R [ Without parenthesis: P + Q'  R ]

## Slide 10: 5. Laws of Boolean Algebra
Identity laws | 
A + 0 = 0 + A = A | A  1 = 1  A = A
Inverse/complement laws | 
A + A' = 1 | A  A' = 0
Commutative laws | 
A + B = B + A | A  B = B  A
Associative laws | 
A + (B + C) = (A + B) + C | A  (B  C) = (A  B)  C
Distributive laws | 
A  (B + C) = (A  B) + (A  C) | A + (B  C) = (A + B)  (A + C)

## Slide 11: 6. Duality
If the AND/OR operators and identity elements 0/1 in a Boolean equation are interchanged, it remains valid
Example:
  The dual equation of a+(bc)=(a+b)(a+c) is a(b+c)=(ab)+(ac)
Duality gives free theorems – “two for the price of one”. You prove one theorem and the other comes for free!
Examples:
  If (x+y+z)' = x'y'z' is valid, then its dual is also valid: (xyz)' = x'+y'+z'
  If x+1 = 1 is valid, then its dual is also valid: x0 = 0

## Slide 12: 7. Theorems
Idempotency | 
X + X = X | X  X = X
One element / Zero element | 
X + 1 = 1 | X  0 = 0
Involution | 
( X' )' = X | 
Absorption 1 | 
X + XY = X | X(X + Y) = X
Absorption 2 | 
X + X'Y = X + Y | X(X' + Y) = XY
DeMorgans’ (can be generalised to more than 2 variables) | 
(X + Y)' = X'  Y' | (X  Y)' = X' + Y'
Consensus | 
XY + X'Z + YZ = XY + X'Z | (X+Y)(X'+Z)(Y+Z) = (X+Y)(X'+Z)

## Slide 13: 7. Proving a Theorem
Theorems can be proved using truth table, or by algebraic manipulation using other theorems/laws.
Example: Prove absorption theorem X + XY = X
  X + XY = X1 + XY (by identity)
  = X(1+Y) (by distributivity) = X(Y+1) (by commutativity)
  = X1 (by one element) = X (by identity)
By duality, we can also cite (without proof) that X(X+Y) = X

## Slide 14: 8. Boolean Functions
Examples of Boolean functions (logic equations):
  F1(x,y,z) = xyz'
  F2(x,y,z) = x + y'z
  F3(x,y,z) = x'y'z + x'yz + xy'
  F4(x,y,z) = xy' + x'z
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 1 | 0 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
From the truth table, F3 = F4.
Can you prove F3 = F4 by using Boolean Algebra?
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0


## Slide 15: 9. Complement Functions

Given a Boolean function F, the complement of F, denoted as F', is obtained by interchanging 1 with 0 in the function’s output values.
Example: F1 = xyz'
What is F1' ?
  F1' = (xyz')' = x' + y' + (z')' (DeMorgan’s) = x' + y' + z (Involution)
x | y | z | F1 | F1'
0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
x | y | z | F1 | F1'
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1

## Slide 16: 10. Standard Forms (1/2)
Certain types of Boolean expressions lead to circuits that are desirable from an implementation viewpoint.
Two standard forms:
  Sum-of-Products (SOP)
  Product-of-Sums (POS)
Literals
  A Boolean variable on its own or in its complemented form
  Examples: (1) x, (2) x', (3) y, (4) y'
Product term
  A single literal or a logical product (AND) of several literals
  Examples: (1) x, (2) xyz', (3) A'B, (4) AB, (5) dg'vw

## Slide 17: 10. Standard Forms (2/2)
Sum term
  A single literal or a logical sum (OR) of several literals
  Examples: (1) x, (2) x+y+z', (3) A'+B, (4) A+B, (5) c+d+h'+j
Sum-of-Products (SOP) expression
  A product term or a logical sum (OR) of several product terms
  Examples: (1) x, (2) x + yz', (3) xy' + x'yz, (4) AB + A'B', (5) A + B'C + AC' + CD
Product-of-Sums (POS) expression
  A sum term or a logical product (AND) of several sum terms
  Examples: (1) x, (2) x(y+z'), (3) (x+y')(x'+y+z), (4) (A+B)(A'+B'), (5) (A+B+C)D'(B'+D+E')
Every Boolean expression can be expressed in SOP or POS form.
DLD page 59 Quick Review Questions Questions 3-2 to 3-5.

## Slide 18: Quiz Time!

Put the right ticks in the following table.
Expression | SOP? | POS?
X'∙Y + X∙Y' + X∙Y∙Z |  | 
(X+Y')∙(X'+Y)∙(X'+Z') |  | 
X' + Y + Z |  | 
X∙(W' + Y∙Z) |  | 
X∙Y∙Z' |  | 
W∙X'∙Y + V∙(X∙Z + W') |  | 












SOP expr: A product term or a logical sum (OR) of several product terms.
POS expr: A sum term or a logical product (AND) of several sum terms.

## Slide 19: 11. Minterms and Maxterms (1/2)
A minterm of n variables is a product term that contains n literals from all the variables.
  Example: On 2 variables x and y, the minterms are:
  x'∙y', x'∙y, x∙y' and x∙y
A maxterm of n variables is a sum term that contains n literals from all the variables.
  Example: On 2 variables x and y, the maxterms are:
  x'+y', x'+y, x+y' and x+y
In general, with n variables we have up to 2n minterms and 2n maxterms.

## Slide 20: 11. Minterms and Maxterms (2/2)
The minterms and maxterms on 2 variables are denoted by m0 to m3 and M0 to M3 respectively.
Each minterm is the complement of the corresponding maxterm
  Example: m2 = x∙y' m2' = ( x∙y' )' = x' + ( y' )' = x' + y = M2
x | y | Minterms |  | Maxterms | 
 |  | Term | Notation | Term | Notation
0 | 0 | x'∙y' | m0 | x+y | M0
0 | 1 | x'∙y | m1 | x+y' | M1
1 | 0 | x∙y' | m2 | x'+y | M2
1 | 1 | x∙y | m3 | x'+y' | M3

## Slide 21: 12. Canonical Forms
Canonical/normal form: a unique form of representation.
  Sum-of-minterms = Canonical sum-of-products
  Product-of-maxterms = Canonical product-of-sums

## Slide 22: 12.1 Sum-of-Minterms
Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain sum-of-minterms expression by gathering the minterms of the function (where output is 1).
F3 = x'∙y'∙z + x'∙y∙z + x∙y'∙z' + x∙y'∙z = m1 + m3 + m4 + m5 = Sm(1,3,4,5) or Sm(1,3 – 5)
F1 = x∙y∙z' = m6
F2 = x'∙y'∙z + x∙y'∙z' + x∙y'∙z + x∙y∙z' + x∙y∙z = m1 + m4 + m5 + m6 + m7 = Sm(1,4,5,6,7) or Sm(1,4 – 7)


## Slide 23: 12.2 Product-of-Maxterms

Given a truth table, example:
x | y | z | F1 | F2 | F3
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0
Obtain product-of-maxterms expression by gathering the maxterms of the function (where output is 0).
F3 = (x+y+z) ∙ (x+y'+z) ∙ (x'+y'+z) ∙ (x'+y'+z') = M0 ∙ M2 ∙ M6 ∙ M7 = PM(0,2,6,7)
F2 = (x+y+z) ∙ (x+y'+z) ∙ (x+y'+z') = M0 ∙ M2 ∙ M3 = PM(0,2,3)

## Slide 24: 12.3 Conversion of Standard Forms
We can convert between sum-of-minterms and product-of-maxterms easily
Example: F2 = Sm(1,4,5,6,7) = PM(0,2,3)
Why? See F2' in truth table.
x | y | z | F2 | F2'
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
F2' = m0 + m2 + m3 Therefore, F2 = (m0 + m2 + m3)' = m0' ∙ m2' ∙ m3' (by DeMorgan’s) = M0 ∙ M2 ∙ M3 (as mx' = Mx)
  Read up DLD section 3.4, pg 57 – 58.
  Quick Review Questions: pg 60 – 61, Q3-6 to 3-13.

## Slide 25: End of File