## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #16
Quine-McCluskey

## Slide 2: Lecture #16: Quine-McCluskey
This topic is only for your own reading only.
A tabulation method similar in concept to K-map
Applicable for functions with any number of variables
  K-maps are useful for functions with at most 5 or 6 variables
Tedious on paper, but can be automated (programmed)
Non-examinable
  But knowing it may enhance your understanding of K-maps

## Slide 3: PIs and EPIs
To find the simplest SOP expression from a K-map, you need to obtain:
  Minimum number of literals per product term; and
  Minimum number of product terms.
Achieved through K-map using
  Biggest groupings of minterms (prime implicants) where possible; and
  No redundant groupings (look for essential prime implicants)

## Slide 4: Eg: F(A,B,C,D) = m(2,3,4,5,7,8,10,13,15)
Step 1: List out all minterms in groups with same number of 1s in their binary codes.
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
1
1
1st column
2: 0010
4: 0100
8: 1000
------------
3: 0011
5: 0101
10: 1010
------------
7: 0111
13: 1101
------------
15: 1111
Codes with one 1
Codes with two 1s
Codes with three 1s
Codes with four 1s

## Slide 5: Eg: F(A,B,C,D) = m(2,3,4,5,7,8,10,13,15)
Step 2: Combine codes that differ by 1 bit into bigger group, write the combined code in next column.
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
1
1
1st column
2: 0010
4: 0100
8: 1000
------------
3: 0011
5: 0101
10: 1010
------------
7: 0111
13: 1101
------------
15: 1111
2nd column


2,10: -010
------------------
2,3: 001-




4,5: 010-


8,10: 10-0


3,7: 0-11








5,7: 01-1
5,13: -101
7,15: -111
13,15: 11-1
Codes with one 1
Codes with two 1s
------------------
Codes with three 1s

## Slide 6: Eg: F(A,B,C,D) = m(2,3,4,5,7,8,10,13,15)
Step 3: Repeat step 2 – Combine codes that differ by 1 bit into bigger group, write the combined code in next column.
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
1
1
1st column
2: 0010
4: 0100
8: 1000
------------
3: 0011
5: 0101
10: 1010
------------
7: 0111
13: 1101
------------
15: 1111

2nd column
2,3: 001-
2,10: -010
4,5: 010-
8,10: 10-0
----------------
3,7: 0-11
5,7: 01-1
5,13: -101
----------------
7,15: -111
13,15: 11-1








3rd column
5,7,13,15: -1-1


5,7,13,15: -1-1


We have completed Phase 1: Identifying all the Prime Implicants (PIs)!

## Slide 7: Eg: F(A,B,C,D) = m(2,3,4,5,7,8,10,13,15)
Phase 2: Identify the Essential Prime Implicants (EPIs)
Draw the PI chart
1
1
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
 | 2 | 3 | 4 | 5 | 7 | 8 | 10 | 13 | 15
2,3: 001- (A'.B'.C) |  |  |  |  |  |  |  |  | 
2,10: -101 (B.C'.D) |  |  |  |  |  |  |  |  | 
4,5: 010- (A'.B.C') |  |  |  |  |  |  |  |  | 
8,10: 10-0 (A.B'.D') |  |  |  |  |  |  |  |  | 
3,7: 0-11 (A'.C.D) |  |  |  |  |  |  |  |  | 
5,7,13,15: -1-1 (B.D) |  |  |  |  |  |  |  |  | 
Where are the EPIs?
Look for columns containing a single tick.
EPI
EPI
EPI
EPIs are: A'.B.C', A.B'.D', and B.D
But we are not done yet. There are still minterms not covered by the EPIs!

## Slide 8: Eg: F(A,B,C,D) = m(2,3,4,5,7,8,10,13,15)
Phase 2: After identifying the EPIs
Draw the reduced PI chart if there are minterms not covered
1
1
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
 | 2 | 3 | 4 | 5 | 7 | 8 | 10 | 13 | 15
2,3: 001- (A'.B'.C) |  |  |  |  |  |  |  |  | 
2,10: -101 (B.C'.D) |  |  |  |  |  |  |  |  | 
4,5: 010- (A'.B.C') |  |  |  |  |  |  |  |  | 
8,10: 10-0 (A.B'.D') |  |  |  |  |  |  |  |  | 
3,7: 0-11 (A'.C.D) |  |  |  |  |  |  |  |  | 
5,7,13,15: -1-1 (B.D) |  |  |  |  |  |  |  |  | 
1. Find out what are the minterms covered by the EPIs.
EPI
EPI
EPI
2. Remove the EPIs and minterms they cover from the chart  reduced PI chart.
3. Find the minimum number of remaining PIs to cover the remaining minterms.
Answer:
B.D + A'.B.C' + A.B'.D' + A'.B'.C

## Slide 9: End of File