## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #22
Cache
Part I: Direct Mapped Cache

## Slide 2: Lecture #22: Cache I: Direct Mapped Cache
Introduction
Cache
  2.1 Locality
  2.2 Memory Access Time
Memory to Cache Mapping
Direct Mapping
Reading Data (Memory Load)
Types of Cache Misses
Writing Data (Memory Store)
Write Policy

## Slide 3: 1. Data Transfer: The Big Picture
Registers are in the datapath of the processor. If operands are in memory we have to load them to processor (registers), operate on them, and store them back to memory.
Memory
Computer
Processor
Control
Devices
Input
Output
Datapath
+
Registers
Store to memory
Load from memory

## Slide 4: 1. Memory Technology: 1950s
1948: Maurice Wilkes examining
EDSAC’s delay line memory tubes
16-tubes each storing 32 17-bit words
Maurice Wilkes: 2005
1952: IBM 2361 16KB magnetic core memory

## Slide 5: 1. Memory Technology Today: DRAM
DDR SDRAM
  Double Data Rate
  – Synchronous Dynamic RAM
  The dominant memory technology in PC market
  Delivers memory on the positive and negative edge of a clock (double rate)
  Generations:
    DDR (MemClkFreq x 2(double rate) x 8 words)
    DDR2 (MemClkFreq x 2(multiplier) x 2 x 8 words)
    DDR3 (MemClkFreq x 4(multiplier) x 2 x 8 words)
    DDR4 (due 2014)

## Slide 6: 1. DRAM Capacity Growth
Unprecedented growth in density, but we still have a problem

## Slide 7: 1. Processor-DRAM Performance Gap
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Performance
Time
“Moore’s Law”
Memory Wall:
1GHz Processor  1 ns per clock cycle
50ns for DRAM access  50 processor clock cycles per memory access!
Gordon Moore noticed that the number of transistors per square inch on integrated circuits had doubled every year/18 months since their invention.

## Slide 8: 1. Faster Memory Technology: SRAM
SRAM
6 transistors per memory cell
 Low density
Fast access latency of 0.5 – 5 ns
More costly
Uses flip-flops
DRAM
1 transistor per memory cell
 High density
Slow access latency of 50-70ns
Less costly
Used in main memory
A SRAM Cell

## Slide 9: 1. Slow Memory Technology: Magnetic Disk
Typical high-end hard disk:
Average Latency: 4 - 10 ms
Capacity: 500-2000GB

## Slide 10: 1. Quality vs Quantity
 | Capacity | Latency | Cost/GB
Register | 100s Bytes | 20 ps | $$$$
SRAM | 100s KB | 0.5-5 ns | $$$
DRAM | 100s MB | 50-70 ns | $
Hard Disk | 100s GB | 5-20 ms | Cents
Ideal | 1 GB | 1 ns | Cheap
Memory
(DRAM)
Devices
Input
Output
Processor
Control
Datapath
Registers
(Harddisk)

## Slide 11: 1. Best of Both Worlds
What we want:
  A BIG and FAST memory
  Memory system should perform like 1GB of SRAM (1ns access time) but cost like 1GB of slow memory
Key concept:
Use a hierarchy of memory technologies:
  Small but fast memory near CPU
  Large but slow memory farther away from CPU

## Slide 12: 1. Memory Hierarchy
Size
SRAM
DRAM
Harddisk
Speed
Registers

## Slide 13: 2. Cache: The Library Analogy
Imagine you are forced to put back a book to its bookshelf before taking another book…….

## Slide 14: 2. Solution: Book on the Desk!
What if you are allowed to take the books that are likely to be needed soon with you and place them nearby on the desk?

## Slide 15: 2. Cache: The Basic Idea
Keep the frequently and recently used data in smaller but faster memory
Refer to bigger and slower memory:
    Only when you cannot find data/instruction in the faster memory
Why does it work?
Principle of Locality
Program accesses only a small portion of the
memory address space within a small time interval

## Slide 16: 2.1 Cache: Types of Locality
Temporal locality
  If an item is referenced, it will tend to be referenced again soon
Spatial locality
  If an item is referenced, nearby items will tend to be referenced soon
Different locality for
  Instructions
  Data

## Slide 17: 2.1 Working Set: Definition
Set of locations accessed during t
Different phases of execution may use different working sets
Our aim is to capture the working set and keep it in the memory closest to CPU

## Slide 18: 2.2 Two Aspects of Memory Access
How to make SLOW main memory appear faster?
  Cache – a small but fast SRAM near CPU
  Hardware managed: Transparent to programmer
How to make SMALL main memory appear bigger than it is?
  Virtual memory
  OS managed: Transparent to programmer
  Not in the scope of this module (covered in CS2106)
Memory
(DRAM)
Devices
Input
Output
Processor
Control
Datapath
Registers
Cache
(SRAM)
(Harddisk)

## Slide 19: 2.2 Memory Access Time: Terminology
Memory
Processor
Cache
X
Y
Hit: Data is in cache (e.g., X)
  Hit rate: Fraction of memory accesses that hit
  Hit time: Time to access cache
Miss: Data is not in cache (e.g., Y)
  Miss rate = 1 – Hit rate
  Miss penalty: Time to replace cache block + hit time
Hit time < Miss penalty

## Slide 20: 2.2 Memory Access Time: Formula
Average Access Time
= Hit rate x Hit Time + (1-Hit rate) x Miss penalty
Example:
Suppose our on-chip SRAM (cache) has 0.8 ns access time, but the fastest DRAM (main memory) we can get has an access time of 10ns. How high a hit rate do we need to sustain an average access time of 1ns?

Let h be the desired hit rate.
1 = 0.8h + (1 – h)  (10 + 0.8) = 0.8h + 10.8 – 10.8h
10h = 9.8  h = 0.98
Hence we need a hit rate of 98%.

## Slide 21: 3. Memory to Cache Mapping (1/2)
Cache Block/Line:
  Unit of transfer between memory and cache
Block size is typically one or more words
  e.g.: 16-byte block  4-word block
  32-byte block  8-word block
Why is the block size bigger than word size?

## Slide 22: 3. Memory to Cache Mapping (2/2)
..00000
..00001
..00010
..00011
..00100
..00101
..00110
..00111
..01000
..01001
..01010
..01011
..01100
..01101
..01110
..01111
Address
Word0
Word1
Word2
Word3
Block0
Block1
8-byte blocks
Observations:
2N-byte blocks are aligned at 2N-byte boundaries
The addresses of words within a 2N-byte block have identical (32-N) most significant bits (MSB).
Bits [31:N]  the block number
Bits [N-1:0]  the byte offset within a block
Memory Address
31
0
N-1
N
Block Number
Offset
Block
Word
Byte

## Slide 23: 4. Direct Mapping Analogy
Imagine there are 26 “locations” on the desk to store books. A book’s location is determined by the first letter of its title.
 Each book has exactly one location.

## Slide 24: 4. Direct Mapped Cache: Cache Index
Mapping Function:
Cache Index
= (BlockNumber) modulo
(NumberOfCacheBlocks)
Observation:
If Number of Cache Blocks = 2M
 the last M bits of the block number is the cache index
Example:
Cache has 22 = 4 blocks
 last 2 bits of the block number is the cache index.
Index
00
01
10
11
Cache Index
Cache
One block
..00000
..00001
..00010
..00011
..00100
..00101
..00110
..00111
..01000
..01001
..01010
..01011
..01100
..01101
..01110
..01111
Block Number (Not Address!)
Memory
One block

## Slide 25: 4. Direct Mapped Cache: Cache Tag
Mapping Function:
Cache Index
= (BlockNumber) modulo
(NumberOfCacheBlocks)
Observation:
Multiple memory blocks can map to the same cache block
 Same Cache Index
However, they have unique tag number:
Tag = Block number / Number of Cache Blocks
Memory
..00000
..00001
..00010
..00011
..00100
..00101
..00110
..00111
..01000
..01001
..01010
..01011
..01100
..01101
..01110
..01111
Block Number (Not Address!)
One block
00
01
10
11
Cache Index
Cache
One block
Tag

## Slide 26: 4. Direct Mapped Cache: Mapping
Cache Block size = 2N bytes
Number of cache blocks = 2M
Offset = N bits
Index = M bits
Tag = 32 – (N + M) bits
Cache Block size = 2N bytes
Memory Address
31
0
N-1
N
Block Number
Offset
N+M-1
Memory Address
31
0
N-1
N
Tag
Offset
Index

## Slide 27: 4. Direct Mapped Cache: Cache Structure
Cache
00
01
10
11
Index
Data
Tag
Valid
Along with a data block (line), cache also contains the following administrative information (overheads):
Tag of the memory block
Valid bit indicating whether the cache line contains valid data
When is there a cache hit?
( Valid[index] = TRUE ) AND ( Tag[ index ] = Tag[ memory address ] )

## Slide 28: 4. Cache Mapping: Example
Memory
4GB
Memory Address
31
0
N-1
N
Block Number
Offset
1 Block
= 16 bytes
Cache
16KB
1 Block
= 16 bytes
N+M-1
31
0
N-1
N
Tag
Offset
Index
Offset, N = 4 bits
Block Number = 32 – 4 = 28 bits
Check: Number of Blocks = 228
Number of Cache Blocks
= 16KB / 16bytes = 1024 = 210
Cache Index, M = 10bits
Cache Tag = 32 – 10 – 4 = 18 bits

## Slide 29: 4. Cache Circuitry: Example
10
Index
18
Tag
Hit
Data
32
16-KB cache: 4-word (16-byte) blocks
31 30 . . . 15 14 13 . . . 5 4 3 2 1 0
Tag
Index
Ofst
0
1
2
.
.
.
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Cache Hit =
[Tag Matches] AND [Valid]
18
MUX
Block offset
2 (Addr[3:2])

## Slide 30: 5. Reading Data: Setup
Given a direct mapped 16KB cache:
  16-byte blocks x 1024 cache blocks
Trace the following memory accesses:
13
31
0
3
4
000000000000000000
0100
Tag
Offset
0000000001
Index
14
000000000000000000
1100
0000000001
000000000000000000
0100
0000000011
000000000000000010
1000
0000000001
000000000000000000
0000
0000000001

## Slide 31: 5. Reading Data: Initial State
Intially cache is empty
   All valid bits are zeroes (false)
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 32: 5. Reading Data: Load #1-1
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index
Load from
Step 1. Check Cache Block at index 1
000000000000000000
0100
Tag
Offset
0000000001
Index

## Slide 33: 5. Reading Data: Load #1-2
Load from
Step 2. Data in block 1 is invalid [Cold/Compulsory Miss]
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 34: 5. Reading Data: Load #1-3
Load from
Step 3. Load 16 bytes from memory; Set Tag and Valid bit
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 35: 5. Reading Data: Load #1-4
Load from
Step 4. Return Word1 (byte offset = 4) to Register
000000000000000000
0100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 36: 5. Reading Data: Load #2-1
Load from
Step 1. Check Cache Block at index 1
000000000000000000
1100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 37: 5. Reading Data: Load #2-2
Load from
Step 2. [Cache Block is Valid] AND [Tags match]  Cache hit!
000000000000000000
1100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 38: 5. Reading Data: Load #2-3
Load from
Step 3. Return Word3 (byte offset = 12) to Register [Spatial Locality]
000000000000000000
1100
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 39: 5. Reading Data: Load #3-1
Load from
Step 1. Check Cache Block at index 3
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 40: 5. Reading Data: Load #3-2
Load from
Step 2. Data in block 3 is invalid [Cold/Compulsory Miss]
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
Index

## Slide 41: 5. Reading Data: Load #3-3
Load from
Step 3. Load 16 bytes from memory; Set Tag and Valid bit
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 42: 5. Reading Data: Load #3-4
Load from
Step 4. Return Word1 (byte offset = 4) to Register
000000000000000000
0100
Tag
Offset
0000000011
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 43: 5. Reading Data: Load #4-1
Load from
Step 1. Check Cache Block at index 1
000000000000000010
1000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 44: 5. Reading Data: Load #4-2
Load from
Step 2. Cache block is Valid but Tags mismatch [Cold miss]
000000000000000010
1000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 45: 5. Reading Data: Load #4-3
Load from
Step 3. Replace block 1 with new data; Set Tag
000000000000000010
1000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 46: 5. Reading Data: Load #4-4
Load from
Step 4. Return Word2 (byte offset = 8) to Register
000000000000000010
1000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 47: 5. Reading Data: Load #5-1
Load from
Step 1. Check Cache Block at index 1
000000000000000000
0000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 48: 5. Reading Data: Load #5-2
Load from
Step 2. Cache block is Valid but Tags mismatch [Cold miss]
000000000000000000
0000
Tag
Offset
0000000001
Index
0
2
1
E
F
G
H
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 49: 5. Reading Data: Load #5-3
Load from
Step 3. Replace block 1 with new data; Set Tag
000000000000000000
0000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 50: 5. Reading Data: Load #5-4
Load from
Step 4. Return Word0 (byte offset = 0) to Register
000000000000000000
0000
Tag
Offset
0000000001
Index
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
1
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15

## Slide 51: 5. Reading Data: Summary
Read address (RA) sent from processor  cache
In cache?
Access memory block at RA
Use Offset and delivery data to processor
Load into cache line
Set Tag and Valid bit (if needed)
Allocate cache line
Read Hit
[Tags Match] AND [Valid]
Read Miss
[Tags Mismatch] OR [!Valid]

## Slide 52: 6. Types of Cache Misses
Compulsory misses
  On the first access to a block; the block must be brought into the cache
  Also called cold start misses or first reference misses
Conflict misses
  Occur in the case of direct mapped cache or set associative cache, when several blocks are mapped to the same block/set
  Also called collision misses or interference misses
Capacity misses
  Occur when blocks are discarded from cache as cache cannot contain all blocks needed

## Slide 53: Exercise #1: Setup Information
Memory
4GB
Memory Address
31
0
N-1
N
Block Number
Offset
1 Block
= 8 bytes
Cache
32Bytes
1 Block
= 8 bytes
N+M-1
31
0
N-1
N
Tag
Offset
Index
Offset, N =
Block Number =
Number of Cache Blocks =
Cache Index, M =
Cache Tag =

3
29
4
2
27

## Slide 54: Exercise #2: Tracing Memory Accesses
Using the given setup in exercise #1, trace the following memory loads:
  Load from addresses:
  4, 0, 8, 12, 36, 0, 4
Note that “A”, “B”…. “J” represent word-size data
  Assume 1 word = 4 bytes
Memory Content
Addr | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
… | …

## Slide 55: Exercise #2: Load #1

Addr. | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
Addresses: 4, 0, 8, 12, 36, 0, 4
Index | Valid | Tag | Word0 | Word1
0 | 0 |  |  | 
1 | 0 |  |  | 
2 | 0 |  |  | 
3 | 0 |  |  | 
Address 4 =
00000000000000000000000000
100
Tag
Offset
00
Index
A
B
0
1
Miss

## Slide 56: Exercise #2: Load #2

Addr. | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
Addresses: 4, 0, 8, 12, 36, 0, 4
Index | Valid | Tag | Word0 | Word1
0 | 1 | 0 | A | B
1 | 0 |  |  | 
2 | 0 |  |  | 
3 | 0 |  |  | 
Address 0 =
00000000000000000000000000
000
Tag
Offset
00
Index
Miss
Hit

## Slide 57: Exercise #2: Load #3

Addr. | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
Addresses: 4, 0, 8, 12, 36, 0, 4
Index | Valid | Tag | Word0 | Word1
0 | 1 | 0 | A | B
1 | 0 |  |  | 
2 | 0 |  |  | 
3 | 0 |  |  | 
Address 8 =
00000000000000000000000000
000
Tag
Offset
01
Index
Miss
Hit
C
D
0
1
Miss

## Slide 58: Exercise #2: Load #4

Addr. | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
Addresses: 4, 0, 8, 12, 36, 0, 4
Index | Valid | Tag | Word0 | Word1
0 | 1 | 0 | A | B
1 | 1 | 0 | C | D
2 | 0 |  |  | 
3 | 0 |  |  | 
Address 12 =
00000000000000000000000000
100
Tag
Offset
01
Index
Miss
Hit
Miss
Hit

## Slide 59: Exercise #2: Load #5

Addr. | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
Addresses: 4, 0, 8, 12, 36, 0, 4
Index | Valid | Tag | Word0 | Word1
0 | 1 | 0 | A | B
1 | 1 | 0 | C | D
2 | 0 |  |  | 
3 | 0 |  |  | 
Address 36 =
00000000000000000000000001
100
Tag
Offset
00
Index
Miss
Hit
Miss
Hit
I
J
1
Miss

## Slide 60: Exercise #2: Load #6

Addr. | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
Addresses: 4, 0, 8, 12, 36, 0, 4
Index | Valid | Tag | Word0 | Word1
0 | 1 | 0 | A | B
1 | 1 | 0 | C | D
2 | 0 |  |  | 
3 | 0 |  |  | 
Address 0 =
00000000000000000000000000
000
Tag
Offset
00
Index
I
J
1
Miss
Hit
Miss
Hit
Miss
A
B
0
Miss

## Slide 61: Exercise #2: Load #7

Addr. | Data
0 | A
4 | B
8 | C
12 | D
… | …
32 | I
36 | J
Addresses: 4, 0, 8, 12, 36, 0, 4
Index | Valid | Tag | Word0 | Word1
0 | 1 | 0 | A | B
1 | 1 | 0 | C | D
2 | 0 |  |  | 
3 | 0 |  |  | 
Address 4 =
00000000000000000000000000
100
Tag
Offset
00
Index
I
J
1
A
B
0
Miss
Hit
Miss
Hit
Miss
Miss
Hit

## Slide 62: 7. Writing Data: Store #1-1
Store X to
Step 1. Check Cache Block 1
1
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
000000000000000000
1000
Tag
Offset
0000000001
Index

## Slide 63: 7. Writing Data: Store #1-2
Store X to
Step 2. [Cache Block is Valid] AND [Tags match]  Cache hit!
1
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
000000000000000000
1000
Tag
Offset
0000000001
Index

## Slide 64: 7. Writing Data: Store #1-3
Store X to
Step 2. Replace Word2 (offset = 8) with X
1
0
0
1
A
B
C
D
0
0
1
I
J
K
L
0
0
0
0
... ... ... … … … … …
0
2
3
4
5
1022
1023
Index
Valid
Tag
Data
Word0
Word1
Word2
Word3
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
000000000000000000
1000
Tag
Offset
0000000001
Index
X
See any problem here?

## Slide 65: 8. Changing Cache Content: Write Policy
Cache and main memory are inconsistent
  Modified data only in cache, not in memory!
Solution 1: Write-through cache
  Write data both to cache and to main memory
Solution 2: Write-back cache
  Only write to cache
  Write to main memory only when cache block is replaced (evicted)

## Slide 66: 8. Write-Through Cache
Problem:
  Write will operate at the speed of main memory!
Solution:
  Put a write buffer between cache and main memory
    Processor: writes data to cache + write buffer
    Memory controller: write contents of the buffer to memory
Processor
Cache
Write Buffer
DRAM

## Slide 67: 8. Write-Back Cache
Problem:
  Quite wasteful if we write back every evicted cache blocks
Solution:
  Add an additional bit (Dirty bit) to each cache block
  Write operation will change dirty bit to 1
    Only cache block is updated, no write to memory
  When a cache block is replaced:
    Only write back to memory if dirty bit is 1

## Slide 68: 8. Handling Cache Misses
On a Read Miss:
  Data loaded into cache and then load from there to register
Write Miss option 1: Write allocate
  Load the complete block into cache
  Change only the required word in cache
  Write to main memory depends on write policy
Write Miss option 2: Write around
  Do not load the block to cache
  Write directly to main memory only

## Slide 69: 8. Writing Data: Summary
Write address (WA) and value sent from processor  cache
In cache?
Depends on
Write Miss Policy
(Write Allocate) or (Write Around)
Depends on
Write Policy
(Write Back)
or (Write Through)
Write Hit
[Tags Match] AND [Valid]
Write Miss
[Tags Mismatch] OR [!Valid]

## Slide 70: Summary
Memory hierarchy gives the illusion of a fast and big memory
Hardware-managed cache is an integral component of today’s processors
Next lecture: How to improve cache performance

## Slide 71: Reading
Large and Fast: Exploiting Memory Hierarchy
  Chapter 7 sections 7.1 – 7.2 (3rd edition)
  Chapter 5 sections 5.1 – 5.2 (4th edition)

## Slide 72: End of File