## Slide 1: CS2100
Tutorial #10
Pipelining
(Prepared by: Aaron Tan)

## Slide 2
Q1.
 | Stage Timing (for 5 stages) | Latency of pipeline register
a. | 300ps, 100ps, 200ps, 300ps, 100ps | 0ps
b. | 200ps, 200ps, 200ps, 200ps, 200ps | 40ps
c. | 200ps, 200ps, 200ps, 200ps, 200ps | 0ps
 | CTseq | CTpipeline | Speedup (10 inst) | Speedup (10m inst)
a. | 1000ps | 300ps | (100010)/(30014) = 2.38 | (100010m)/(300(10m+4)) = 3.33
b. | 1000ps | 240ps | (100010)/(24014) = 2.98 | (100010m)/(240(10m+4)) = 4.17
c. | 1000ps | 200ps | (100010)/(20014) = 3.57 | (100010m)/(200(10m+4)) = 5.00 (ideal)

## Slide 3
Q2.
# register $s0 contains a 32-bit value
# register $s1 contains a non-zero 8-bit value
# at the right most (least significant) byte
add $t0, $s0, $zero #inst A
add $s2, $zero, $zero #inst B
lp: bne $s2, $zero, done #inst C
beq $t0, $zero, done #inst D
andi $t1, $t0, 0xFF #inst E
bne $s1, $t1, nt #inst F
addi $s2, $s2, 1 #inst G
nt: srl $t0, $t0, 8 #inst H
j lp #inst J
done:
$s0 = 0xAFAFFAFA
$s1 = 0xFF
$s2 = 0
$t0 = 0xAFAFFAFA
0xAFAFFAFA ($t0)
& 0x000000FF
0x000000FA ($t1)

## Slide 4
Q2a.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
add $t0, $s0, $0 | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $s2, $0, $0 |  | F | D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lp: bne $s2, $0, done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t0, $0, done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
andi $t1, $t0, 0xFF |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $s1, $t1, nt |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $s2, $s2, 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
nt: srl $t0, $t0, 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data forwarding. No control hazard mechanism.
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
20 cycles
Note that the addi instruction is not executed.
3 cycles of delay
3 cycles of delay
3 cycles of delay

## Slide 5
Q2b.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
add $t0, $s0, $0 | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
add $s2, $0, $0 |  | F | D |  |  |  |  |  |  |  |  |  |  |  | 
lp: bne $s2, $0, done |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t0, $0, done |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
andi $t1, $t0, 0xFF |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
bne $s1, $t1, nt |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $s2, $s2, 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
nt: srl $t0, $t0, 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
j lp |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
nt: srl $t0, $t0, 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data forwarding. Branch prediction – predict not taken.
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
*
*
F
D
E
M
W
14 cycles
F
D
*
*
*
F
*
*
*
*

## Slide 6
Q2c.
Early branching. Swap two instructions.
add $t0, $s0, $zero
add $s2, $zero, $zero
lp: bne $s2, $zero, done
beq $t0, $zero, done
andi $t1, $t0, 0xFF
bne $s1, $t1, nt
addi $s2, $s2, 1
nt: srl $t0, $t0, 8
j lp
done:
?

## Slide 7
Q2c.
Early branching. Swap two instructions.
add $t0, $s0, $zero
add $s2, $zero, $zero
lp: bne $s2, $zero, done
beq $t0, $zero, done
andi $t1, $t0, 0xFF
bne $s1, $t1, nt
addi $s2, $s2, 1
nt: srl $t0, $t0, 8
j lp
done:
add $s2, $zero, $zero
add $t0, $s0, $zero
lp: bne $s2, $zero, done
beq $t0, $zero, done
andi $t1, $t0, 0xFF
bne $s1, $t1, nt
addi $s2, $s2, 1
nt: srl $t0, $t0, 8
j lp
done:

## Slide 8
Q2c.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
add $t0, $s0, $0 | F | D | E | M | W |  |  | 
add $s2, $0, $0 |  | F | D | E | M | W |  | 
lp: bne $s2, $0, done |  |  | F | D | D | E | M | W
Before swapping:
After swapping:
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
add $s2, $0, $0 | F | D | E | M | W |  |  | 
add $t0, $s0, $0 |  | F | D | E | M | W |  | 
lp: bne $s2, $0, done |  |  | F | D | E | M | W | 
add $t0, $s0, $zero
add $s2, $zero, $zero
lp: bne $s2, $zero, done
beq $t0, $zero, done
andi $t1, $t0, 0xFF
bne $s1, $t1, nt
addi $s2, $s2, 1
nt: srl $t0, $t0, 8
j lp
done:
add $s2, $zero, $zero
add $t0, $s0, $zero
lp: bne $s2, $zero, done
beq $t0, $zero, done
andi $t1, $t0, 0xFF
bne $s1, $t1, nt
addi $s2, $s2, 1
nt: srl $t0, $t0, 8
j lp
done:

## Slide 9
Q2d.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21
add | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lp: bne .. done |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq .. done |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
andi |  |  |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  |  | 
bne .. nt |  |  |  |  |  |  |  |  |  |  |  | F | D | E | M | W |  |  |  |  | 
addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
nt: srl |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | F | D | E | M | W | 
j lp |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | F | D | E | M | W
lp: bne .. done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | F
Data forwarding. No control hazard mechanism.
4 iterations.
Total number of cycles = 2 + (4  18) + 9 = 83 cycles.
18 cycles
$t0 = 0xAFAFFAFA
 0x00AFAFFA
 0x0000AFAF
 0x000000AF
 0x00000000
Compare last 8 bits with 0xFF
lp: bne $s2, $zero, done
beq $t0, %zero, done

## Slide 10
Q2e.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
add $t0, $s0, $0 | F | D | E | M | W |  |  |  |  |  |  |  |  |  | 
add $s2, $0, $0 |  | F | D | E | M | W |  |  |  |  |  |  |  |  | 
lp: bne $s2, $0, done |  |  | F | D | E | M | W |  |  |  |  |  |  |  | 
beq $t0, $0, done |  |  |  | F | D | E | M | W |  |  |  |  |  |  | 
andi $t1, $t0, 0xFF |  |  |  |  | F | D | E | M | W |  |  |  |  |  | 
bne $s1, $t1, nt |  |  |  |  |  | F | D | E | M | W |  |  |  |  | 
addi $s2, $s2, 1 |  |  |  |  |  |  | F | D | E | * | * |  |  |  | 
nt: srl $t0, $t0, 8 |  |  |  |  |  |  |  | F | D | * | * | * |  |  | 
j lp |  |  |  |  |  |  |  |  | F | * | * | * | * |  | 
nt: srl $t0, $t0, 8 |  |  |  |  |  |  |  |  |  | F | D | E | M | W | 
j lp |  |  |  |  |  |  |  |  |  |  | F | D | E | M | W
lp: bne $s2, $0, done |  |  |  |  |  |  |  |  |  |  |  |  |  |  | F
Data forwarding. Branch prediction – predict not taken.
12 cycles
4 iterations.
Total number of cycles = 2 + (4  12) + 6 = 56 cycles.

## Slide 11
Q3.
beq $s2, $zero, End # Inst1
addi $t8, $s2, -1 # Inst2
sll $t8, $t8, 2 # Inst3
Loop: add $t0, $s0, $t8 # Inst4
add $t1, $s1, $t8 # Inst5
lw $t2, 0($t0) # Inst6
lw $t3, 0($t1) # Inst7
andi $t4, $t3, 3 # Inst8
addi $t4, $t4, -3 # Inst9
beq $t4, $zero, A1 # Inst10
add $t2, $t2, $t3 # Inst11
j A2 # Inst12
A1: addi $t2, $t2, 1 # Inst13
A2: sw $t2, 0($t0) # Inst14
addi $t8, $t8, -8 # Inst15
slt $t7, $t8, $zero # Inst16
beq $t7, $zero, Loop # Inst17
End:
What does the code do?
int i;
for (i=n-1; i>=0; i-=2) {
if (B[i]%4 == 3)
A[i] = A[i] + 1;
else
A[i] = A[i] + B[i];
}
$s0 = base address of array A
$s1 = base address of array B
$s2 = n (size of each array)
$t2: A[i]
$t3: B[i]

## Slide 12
Q3a.
beq $s2, $zero, End # Inst1
addi $t8, $s2, -1 # Inst2
sll $t8, $t8, 2 # Inst3
Loop: add $t0, $s0, $t8 # Inst4
add $t1, $s1, $t8 # Inst5
lw $t2, 0($t0) # Inst6
lw $t3, 0($t1) # Inst7
andi $t4, $t3, 3 # Inst8
addi $t4, $t4, -3 # Inst9
beq $t4, $zero, A1 # Inst10
add $t2, $t2, $t3 # Inst11
j A2 # Inst12
A1: addi $t2, $t2, 1 # Inst13
A2: sw $t2, 0($t0) # Inst14
addi $t8, $t8, -8 # Inst15
slt $t7, $t8, $zero # Inst16
beq $t7, $zero, Loop # Inst17
End:
Common: Inst1 – Inst10
Before loop: Inst1 – Inst3
Inside loop: Inst4 – Inst 10
Two paths:
If (B[i]%4 == 3): Inst13, 14, 15, 16, 17
Otherwise: Inst11, 12, 14, 15, 16, 17
100 iterations
Therefore,
Minimum = 3 + 100  12 = 1203
Maximum = 3 + 100  13 = 1303
Arrays A and B each contains 200 integers.

## Slide 13
Q3b.
beq $s2, $zero, End # Inst1
addi $t8, $s2, -1 # Inst2
sll $t8, $t8, 2 # Inst3
Loop: add $t0, $s0, $t8 # Inst4
add $t1, $s1, $t8 # Inst5
lw $t2, 0($t0) # Inst6
lw $t3, 0($t1) # Inst7
andi $t4, $t3, 3 # Inst8
addi $t4, $t4, -3 # Inst9
beq $t4, $zero, A1 # Inst10
add $t2, $t2, $t3 # Inst11
j A2 # Inst12
A1: addi $t2, $t2, 1 # Inst13
A2: sw $t2, 0($t0) # Inst14
addi $t8, $t8, -8 # Inst15
slt $t7, $t8, $zero # Inst16
beq $t7, $zero, Loop # Inst17
End:
Data dependency: I8, I10, I17
Control dependency: I2, I11, I13, I4

## Slide 14
Q3c.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
I1: beq | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I2: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I3: sll |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I4: Loop: add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I5: add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I6: lw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I7: lw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I8: andi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I9: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I10: beq A1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I11: add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I12: j A2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I13: A1: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I14: A2: sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I15: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I16: slt |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I17: beq Loop |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq at Inst10 branches to A1
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
24 cycles

## Slide 15
Q3d.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
I1: beq | F | D | E | M | W |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I2: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I3: sll |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I4: Loop: add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I5: add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I6: lw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I7: lw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I8: andi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I9: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I10: beq A1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I11: add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I12: j A2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I13: A1: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I14: A2: sw |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I15: addi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I16: slt |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
I17: beq Loop |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq at Inst10 does not branch to A1
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
26 cycles

## Slide 16
END OF FILE